Cross Reference - KAS / AKD Capture Engine Parameter Settings

| Item Description | Set in COE Init? | Index Number and Sub Index | Standard PDO? | Setup in WorkBench Capture Screen? | AKD Drive Parameter | Default AKD Drive Value | Change made by default COE Values? | PLCopen support |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CAPTURE ENGINE 1 (inside drive) |  |  |  |  |  |  |  | Trig_REF.InputID = 0 |
| Trigger ID – The drive (Axis) the trigger source comes from | N/A | N/A | No | N/A | N/A | N/A | No | Trig_REF.TrigID |
| Trigger Source (IN1 to IN7, RS485 1 to 3, primary index, tertiary index) | Yes - 0 | 0x3460 1 | No | Yes | CAP0.TRIGGER | 0 | Yes |  |
| Capture Mode (position, time, ECAT DCT, cap zero angle position) | Yes - 2 | 0x3460 3 | No | Yes | CAP0.MODE | 0 | Yes | Trig_REF.TrigMode |
| Pre-Condition Event (Ignore, Trigger edge after precond edge, precond = 0, precond = 1) | Can Add | 0x3460 5 | No | Yes | CAP0.EVENT | 0 | No |  |
| Pre-Condition Trigger Edge (Rising, falling, both) | Can Add | 0x3460 7 | No | Yes | CAP0.PREEDGE | 0 | No |  |
| Pre-Condition Trigger Source (IN1 to IN7, RS485 1 to 3, primary index, tertiary index) | Can Add | 0x3460 9 | No | Yes | CAP0.PRESELECT | 0 | No |  |
| Capture Feedback Source (0=FB1,1=FB2,2=FB3) | Can Add | 0x3460 11 | No | Yes | CAP0.FBSOURCE | 0 | No |  |
| Latch Control – Enables (Arms) the latch (trigger) monitoring | Can Add | 0x20A4 0,1 | Yes | Yes | CAP0.EDGE | 1 | No | Trig_REF.Direction, Trig_REF.TrigID MC_TouchProbe, MC_Reference |
| Latch Control – Command to read the position or time | Can Add | 0x20A4 8,9 | Yes | N/A | CAP0.EN | 0 | No |  |
| Latch Status – Has the rising or falling edge triggered? | N/A | 0x20A5 0,1 | Yes | Yes | CAP1.STATE | 0 | N/A |  |
| Latched value (Position or Time ) | N/A | 0x20A6 | Yes | Yes (drive units) | CAP0.PLFB or CAP0.T | 0 | N/A | MC_TouchProbe.RecordedPosition (position only) |
| CAPTURE ENGINE 2 (inside drive) |  |  |  |  |  |  |  | Trig_REF.InputID = 1 |
| Trigger ID – The drive (Axis) the trigger source comes from | N/A | N/A | No | N/A | N/A | N/A | No | Trig_REF.TrigID |
| Trigger Source (IN1 to IN7, RS485 1 to 3, primary index, tertiary index) | Yes - 1 | 0x3460 2 | No | Yes | CAP1.TRIGGER | 1 | Yes |  |
| Capture Mode (position, time, ECAT DCT, cap zero angle position) | Yes – 2 | 0x3460 4 | No | Yes | CAP1.MODE | 0 | Yes | Trig_REF.TrigMode |
| Pre-Condition Event (Ignore, Trigger edge after precond edge, precond = 0, precond = 1) | Can Add | 0x3460 6 | No | Yes | CAP1.EVENT | 0 | No |  |
| Pre-Condition Trigger Edge (Rising, falling, both) | Can Add | 0x3460 8 | No | Yes | CAP1.PREEDGE | 1 | No |  |
| Pre-Condition Trigger Source (IN1 to IN7, RS485 1 to 3, primary index, tertiary index) | Can Add | 0x3460 10 | No | Yes | CAP1.PRESELECT | 0 | No |  |
| Capture Feedback Source ( 0=FB1,1=FB2,2=FB3) | Can Add | 0x3460 12 | No | Yes | CAP1.FBSOURCE | 0 | No |  |
| Latch Control – Enables (Arms) the latch (trigger)monitoring | Can Add | 0x20A4 2,3 | Yes | Yes | CAP1.EN | 1 | No | Trig_REF.Direction Trig_REF.TrigID MC_TouchProbe, MC_Reference |
| Latch Control – Command to read the position or time | Can Add | 0x20A4 10,11 | Yes | N/A |  | 0 | No |  |
| Latch Status – Has the rising or falling edge triggered? | N/A | 0x20A5 2,3 | Yes | Yes | CAP1.STATE | 0 | N/A |  |
| Latched Value ( Position or Time ) | N/A | Ox20A7 | Yes | Yes (drive units) | CAP1.PLFB or CAP1.T | 0 | N/A | MC_TouchProbe.RecordedPosition (position only) |

Capture Engine (drive capture engine to be used)

INT TriggerInput.InputID

0 = Capture Engine 0

1 = Capture Engine 1

Range is [0,1]

For information on configuring the capture engines, refer to AKD Capture Engine Configuration.

Trigger Direction (input signal’s edge to capture)

INT TriggerInput.Direction

1 = rising edge

2 = falling edge

Range is [1,2]

Axis Number (where input comes from)

INT TriggerInput.TrigID

0 = trigger axis is to be the same as Axis.AXIS_NUM.

Range is [0,256]

Trigger Mode (capture method)

INT TriggerInput.TrigMode

0 = time based capture

1 = position based capture. For position based capture the TrigID must be the same as the Axis_Ref.

Range is [0,1]