GIDDINGS & LEWIS

PiC Application Note

Document Number:  AN000005

Topic: Switch Settings for the A-B 1770-KF2 Module

This document specifies the dip switch settings for the Allen-Bradley 1770-KF2 module used to connect

the PiC to A-B’s Data Highway or Data Highway Plus.  The KF2 module converts the data to RS232

for the PiC.

The KF-2 module has 8 switch banks labeled SW-1, SW-2, ... , SW-8.

SW-1

SW-1 has 5 switches:

1        2        3        4        5

OFF   OFF   OFF   OFF   OFF

These settings specify full duplex, BCC error checking, no parity, no embedded responses, “accept all

messages regardless of duplication”, and “ignore handshaking signals”.

SW-2, SW-3, and SW-4

SW-2, SW-3, and SW-4 have 2 switches, 3 switches, and 3 switches respectively.  These switch banks

specify the node number in octal.  SW-4 specifies the least significant octal digit, SW-3 specifies the next

significant octal digit, and SW-2 specifies the most significant octal digit.  For example, if the node number is 035octal, the switch settings would be:

| Switch Bank | SW-2 | SW-3 | SW-4 |
| --- | --- | --- | --- |
| Octal Node Number | 0 | 3 | 5 |
| Dip Switch | 1 2 | 1 2 3 | 1 2 3 |
| Setting | OFF OFF | OFF ON ON | ON OFF ON |

SW-5

SW-5 has 2 switches:

1       2

ON   ON

This sets the network communication rate to 57,600 bits per second.

SW-6

SW-6 has 4 switches:

1       2      3       4

OFF   ON   ON   ON

This sets communication rate to 9600 bits per second for the KF-2’s asynchronous port and sets “Execute

received diagnostic commands”.

SW-7

SW-7 has 2 switches:

1         2

OFF   OFF   --------> for Data Highway

ON   OFF   --------> for Data Highway Plus

SW-8

SW-8 has 2 switches:

1       2

OFF   ON

This selects RS-232-C interface.

Revision History

Date:  17-Nov-1995

Author:  Mark Kolell

Changes:  Original

Date:  [For each revision, enter the date revised,]

Author:  [the name of the person revising the document,]

Changes:  [and indicate what changes were made.]