GIDDINGS & LEWIS

PiC Application Note

Document Number:  AN000009

Topic:  Communicating to Allen Bradley SLC 500’s

The standard AB Data Highway Plus ASFB product (503-18960-00) is used today to  communicate data between a PLC 5/30 or higher processor and any of the Giddings & Lewis PiC900 family of processors (PiC 9, PiC 90 & PiC 900).  Data includes up to 999 INT’s, REAL’s, and BOOL’s.  This package is also used to communicate to any compatible device or software package adhering to the Allen Bradley DF1 full-duplex serial communication protocol.

The Giddings & Lewis implementation of the DF1 protocol has the following configuration requirements which are also documented in the ASFB manual.

DF1 full-duplex serial communications

BCC error detection

Logical binary addressing

No embedded response support

PLC 5  type messages

The same software product may also be used for communications between a SLC processor and one of the PiC 900 family of processors.  The SLC products that are supported include the SLC 5/03 (rev. C or higher) and the SLC 5/04.  APS v5.11 programming software configured for the OS301 operating system is required to send PLC5 type messages from the SLC.  The only limitation is that all messages must originate from the SLC processor.  Unlike interfacing to a PLC 5 where the PiC can send an unsolicited message to the PLC, the SLC can only send a PLC 5 message - it cannot receive one.  This simply means that the SLC can be programmed to read or write the data in the PiC, but the PiC cannot read or write the data in the SLC.

The basic steps to configure the SLC processor are shown below.  Please note that this information may not be presented in the same format that you would see them when actually configuring a SLC control.  This information is provided to help identify the type of changes that need to be made in the configuration of the processor to communicate with the Giddings & Lewis products.

Configure the processor type and select the OS301 operating system.

Configure the Channel 0 port (9 pin) for the following settings

Channel Configuration

Channel 0 Configuration

Current Communication Mode:	SYSTEM

System Mode Driver:		DF1 Full-Duplex

User Mode Driver:		Generic ASCII

Write Protect:			DISABLED

Mode Changes:			DISABLED

Mode Attention Character:		\1b

System Mode Character:		S

User Mode Character:		U

Edit Resource/File owner Timeout:	60

Pass thru Link ID:		1

Channel 1 Configuration

(Dont’ care)

Configure the System Mode Configuration for Channel 0 to the following settings.

Channel 0 System Mode Configuration

Communication Device:  DF1 Full-Duplex

Diagnostic File:  	RESERVED

Baud Rate:  9600			Parity:	NONE

Duplicate Detect:  DISABLED	Error Detect:  BCC

ACK Timeout:  50		NAK Retries:  3

Source ID:  3			ENQ Retries:  3

Control Line:  No Handshaking	Embedded Responses:  AUTO-DETECT

Program a MSG instruction to initiate a message from the SLC to the PiC.

Type:  Peer-to-Peer

Read/Write:  WRITE

Target Device:  PLC5

Local/Remote:  LOCAL

Control Block:  N7:10

Channel:  0

Target Node:  1

Source File Address:  N7:50

Target Destination File Address:  N7:0

Message Length in Elements:  20

Message Timeout:  2

SLC to PiC cable pinout.

9 pin (SLC chn 0 port)			10 pin (PiC USER port)

1-4-6	Jumper together

7-8	Jumper together

2 -------------------------------------------------10  TXD

3 --------------------------------------------------9   RXD

5 --------------------------------------------------8   GND

Additional information on the configuration and programming of the PiC control is provided in the AB Data Highway Plus ASFB manual.

Revision History

Date:  20-Dec-95

Author:  Todd Vance

Changes:  Original

Date:  27-Feb-95

Author:  Todd Vance

Changes:  Added APS v5.11 and OS301 requirements.  Added SLC configuration guidelines.

Date:  [For each revision, enter the date revised,]

Author:  [the name of the person revising the document,]

Changes:  [and indicate what changes were made.]